## Slide 1: PLR: a software approach to transient fault tolerance for multicore architectures
Ieee transactions on dependable and secure computing, vol.6, n°2, aprile-giugno 2009
Alex Shye, Joseph blomstedt, tipp moseley, vijay janapa reddi e daniel a. connors

## Slide 2: Introduction
Transient faults = event that invert the state of a transistor
The inverted value may propagate to cause an error in program execution
Number of available transistor per chip grows exponentially
Error rate of an entire chip is expected to increase dramatically

## Slide 3: introduction
Custom solutions:
  Add redundancy adding logic to mainframe processor
  Specialized machine with custom hardware and software redundancy
General-purpose systems cannot adopt these customized techniques
  Fault during the execution of a bank transaction
  Fault during graphic processing or audio decoding
Application specific constraints
  Low cost and quick time to market
  Redundancy = cost
Design time and cost constraints
  Fault can appears after design and fabrication
  Altitude, temperature, age , … = higher fault rates
Post-design environment techniques

## Slide 4: introduction
Software reliability techniques are an attractive solution
  Zero hardware design cost
  Flexible deployment
Existing software use the compiler to insert redundant instruction
  Decrease performance
  Recompilation of all application
  Source code is often unavailable
PLR (process-level redundancy) creates a set of redundant process and compares their output
  No additional redundant hardware structures
  Operates transparently to the application

## Slide 5: background
Transient fault can be classified by its effect on system execution
  Benign fault = transient fault that does not propagate to affect the correcteness of an application
  Silent data corruption (SDC) = a transient fault that is undetected and propagates to corrupt program output
  Detected unrecoverable error (DUE) = transient fault detected without the possibility of recovery
    A True DUE occurs when a fault that would propagate to incorrect execution is detected
    A False DUE occurs when a benign fault is detected as a fault

## Slide 6: hardware-centric fault detection
Sphere of replication (SoR) describes a technique’s logical domain of redundancy and specify the boundary for fault detection and containment
  Any data that enters the SoR is replicated
  Any execution within the SoR are redundant in some form
  Any output data is compared before leaving the SoR
The hardware-centric fault detection model view the system as a collection of hardware components

## Slide 7: software-centric fault detection
Software-centric fault detection model is a paradigm in wich the system is viewed as the software layers that must execute correctly
The only faults that matter are the faults that affects software correctness

## Slide 8: Process level redundancy (plr)
Transparency
Software implemented
Software centric
Replica-based

## Slide 9: PLr overview

## Slide 10: Maintaining process semantics
Pid consistency
Correct exit code
Signaling
In order to maintain process semantics, PLR uses a figurehead process
  Sleeps and waits on the redundant processes
  Receives the application’s exit value from the system call emulation unit and exits
  Performs signal forwarding

## Slide 11: Process replicas
During execution one of the redundant processes is logically labeled master the others are slave
At each system call the system call emulation unit is invoked and it performs:
  Input replication
  Output comparison
  Fault recovery
It also ensures that the following requirements are mantained:
  The execution of the redundant process must be transparent to the system environment
  The execution among the redundant processes must be deterministic
  All redundant processes must be identical

## Slide 12: input replication
Any data that passes into the processes is received once by the master process and then passed to the slave processes
During system call emulation, any read data is replicated and copied to the slave processes
The return value from all system calls is considered as input data and is replicated

## Slide 13: output comparison
Must be compared:
  All data that exit the redundant processes
  Any write buffers that will be passed outside the SoR
  Any data passed as a a system call parameter
Small amount of data = copying data to shared memory segment and comparing bytes
Larger write buffers = local creation of a 32-bit CRC and then the CRC value is compared through shared memory

## Slide 14: Emulating system calls
At the beginning of each call to the emulation unit, the type of system call is compared to ensure that all redundant processes are at a common system call
System call emulation unit will perform different tasks in case of different system calls:
  Modify any system state(file renaming, linking, etc) are executed once by the master process.
  In other cases the system call will be called by all processes, once by the master process in its original state and once by each redundant process to emulate the operation

## Slide 15: Shared memory
Potential nondeterminism between redundant processes
Trap and emulate
  Any system calls regarding shared memory is a special case
  PLR updates a shared memory map (SMM)
  PLR switches the protection of all the shared memory pages
  Trap handler in PLR decodes and begins to emulate the instruction
  High overhead
Trap and emulate and probe
  Placing a probe at the offending instruction after a trap
  Emulate a specific instruction

## Slide 16: Asynchronous signals
Another form of potential nondeterminism
Figurehead process take care of the first part of signal processing
Signal handlers are called asynchronously and may read or write any data in the process’s address space
PLR inserts probes and marks specific points in the code as epoch boundaries
An epoch is a timeslice of a program in wich the start and end points are known and identical across the redundant processes
Signal handling is deferred and handled at epoch boundaries

## Slide 17: Asynchronous signals
Figurehead receives the asynchronous signal
It sends a SIGSTOP to all the redundant processes
It inspects the epoch counter of each redundant process
A pending signal is set up to be serviced at an epoch count equal to the largest current epoch counter plus one
It resumes the execution of all redundant processes
The redundant processes execute and, at each epoch boundary, check if there is a pending signal to be handled

## Slide 18: Transient fault detection
Output mismatch
  Transient fault will be detected with the output comparison
Watchdog time-out
  A fault cause an error in control flow, wich calls an errant system call
  Transient fault cause a process to hang indefinitely
Program failure
  Segmentation violation, bus error, illegal instruction
  Signal handlers are set up to catch the corresponding signal

## Slide 19: Transient fault recovery
The killed process are replaced by duplicating a correct process
Output mismatch
  The process with incorrect data are immediately killed
Watchdog time-out
  There is only one process in the emulation unit and it will be killed
  All processes are in the emulation unit except one that will be killed
Program failure
  Incorrect process is already dead

## Slide 20: Windows of vulnerability
All fault tolerance techniques have windows of vulnerability, wich are usually associated with faults to the checker mechanism
Figurehead process is a single point of failure but it performs almost no real work and the probability of a transient fault affecting its execution is very low
A single monitor process also represents a single point of failure but it can be replicated
Although not completely reliable, partial redundancy may be sufficient to improve reliability enough to meet user or vendor reliability standards

## Slide 21: Experimental results
The prototype is built using the Intel Pin dynamic binary instrumentation system
The tool uses Pin to dynamically create redundant processes and PinProbes to intercept system calls
Evaluated running a set of the SPEC2000 benchmarks
One thousand runs are executed per benchmark
For each run a dynamic instruction is used to randomly choose a specific invocation of an instruction to fault (switching a random bit)
Performance is measured by running the prototype with both two and three redundant processes on a four processor system

## Slide 22: Fault injection results
Time-outs of the watch-dog alarm are ignored because they occur very infrequently (∼0,05% of the time)

## Slide 23: Fault propagation

## Slide 24: Performance results
Two redundant processes for fault detection, three to support recovery

## Slide 25: Contention overhead
Sharing memory bandwidth between multiple redundant processes
CPU-bound applications very low overhead vs. memory-bound applications high overhead

## Slide 26: Emulation overhead
PLR technique might be best deployed for specific application domains without significant system call functionality

## Slide 27: Emulation overhead
Evaluates the amount of data at each system call that must be compared between redundant process techniques.

## Slide 28: Shared memory support
Benchmark that periodically writes to a shared memory region

## Slide 29: conclusion
PLR is an attractive alternative in emerging multicore processors
Providing redundancy at the process level, PLR leverages the OS to freely schedule the processes to all available hardware resources
PLR can be deployed without modifications to the application, OS or underlying hardware
PLR’s software centric fault detection model detects faults and safely ignores benign faults
PLR provides fault detection with a 16,9 percent (mean) overhead
Comparable performance to hardware techniques