## Slide 1: Anomaly detection: A survey
Acm computing surveys, vol. 41, n°3, article 15, publication date: july 2009
Varun chandola, arindam banerjee and vipin kumar

## Slide 2: Introduction
The goal is to build an ultrareliable fault-tolerant computer system for aircraft control
Modern commercial jet transports use computers to carry out many functions
The reliability requirement for these computers is that the probability of failure should be less than per hour in a flight of ten hours duration
Highly reliable computer system can have application in other areas as well (i.e. critical industries applications)
The objective in designing SIFT(Software Implemented Fault Tolerance) is to achieve the reliability required in an economic manner
Moreover, the resulting system must be as flexible as possible

## Slide 3: background
Study of the requirements (computational and memory requirements)
Design hardware and software system
Build an engineering model
Testing to demonstrate the fault-tolerant behavior

## Slide 4: System overview

## Slide 5: System overview
The SIFT system executes a set of tasks, each of wich consists of a sequence of iterations
The input data to each iteration of a task is the output data produced by the previous iteration of some collection of tasks (wich may include the task itself)
Each iteration of a task is independently executed by a number of modules
A processor execute the iteration
The processor places the iteration’s output in his memory associated
A processor that uses the output of this iteration determines its value by examining the output generated by each processor wich executed the iteration (typically a «two out of three» votation)

## Slide 6: System overview
Iterative nature of the tasks:
  economize the amount of voting
    voting only at the beginning of each iteration than voting on the results of all calculations
  loose synchronization of the different processors
    an iteration can be scheduled for execution at slightly different times by different processors
    simultaneous transient failures of several processors will be less likely to produce correlated failures in the replicated versions of a task
The number of processors executing a task can vary with the task and can be different for the same task at different times
The allocation of task to modules is determined dinamically by a task called the global executive

## Slide 7: Fault isolation
Preventing a faulty unit from causing incorrect behavior in a nonfaulty unit
Protection against the corruption of data is provided by the way in wich units can communicate
  A processing module can read data from any processing module’s memory, but it can write only in its own memory
Fault isolation also requires that invalid control signals not produce incorrect behavior
  Wrong action
  Not providing service to other units
These two type of fault propagation are prevented by making each unit autonomous, with its own control

## Slide 8: Fault masking
The processor receive multiple copies of the data
Each copy is obtained from a different memory over a different bus and the processor uses majority voting to obtain a correct version of the data
After identifying the faulty unit, the system will be reconfigured
  Faulty processing module  the tasks are reassigned to other modules
  Faulty bus  processors will request their data over other buses

## Slide 9: scheduling
Two types of timing requirements
  Output to the actuators must be generated with specific frequency
  The delay between the reading of sensors and the generation of output to actuators based upon these readings must be kept below specified limits
Iteration rate assigned to each task
The processing of each iteration of the task must be completed within the time frame

## Slide 10: Processor synchronization
Needs 3N+1 clocks to mask any N simultaneous fault
Clock synchronization algorithm
  Each clock computes a vector of clock values, interactive consistency vector
    A clock P set the entry of the vector corresponding to P itself to P’s own value
    The value for the entry of another processor q is obtained as follow
      Read q’s value from q
      Obtain from each other clock r the value of q that r read from q
      Majority agree  majority value used, otherwise NIL (q is faulty)
    Let δ the maximum amount by wich the values may disagree
      Any value greater then δ or NIL is ignored
      P takes the median value of the remaining components as its new value

## Slide 11: Reliability prediction
Markov Model
State labeled by triplet (h,d,f) where h = number of detected failures handled by reconfiguration, d = number of failures detected, f = number of failures occurred
Transitions caused by:
  Fault occurrance
  Fault detection
  Fault handling
Hardware fault, transient faults assume exponential distributions
  Executive system considers unit faulty only after multiple transient fault
  Fail rates: processors = per hour, busses = per hour

## Slide 12: Reliability prediction
Exhaustion of spares =
Double faults (t = 100ms) =
Double faults (t = 1s) =

## Slide 13: The Sift hardware
SIFT system attempts to use standard units whenever possible
Special design is needed only in the bus system and in the interface between the buses and the processing modules

## Slide 14: The software system
Executive software
  Responsible for the reliable execution of the application tasks
    Run each task at the required iteration rate
    Provide correct input values
    Detect errors, diagnose their cause
    Reconfigure system after failure
  3 executive components
    Global executive task
    Local executive
    Local-global communication tasks

## Slide 15: The local-global communication tasks
Local-Global communication tasks consist of reconfiguration task and error reporting task

## Slide 16: The global executive task
Executed as critical task
Analyzes error reports, diagnoses errors
Determines failed processor, reccomend reconfiguration
List of processors reccomended to be reconfigured out of the system is broadcast to reconfiguration task

## Slide 17: The local executive
Collection of routines
  Error handler
    Invoked by voter in case of fault detection
    Updates error table
  Scheduler
    Schedule execution tasks
    Use predefined iteration rate
    Define sequence of time frames
    Whereas execution must occur within a frame, it could be any time during that frame
    Scheduler invoked by timer interrupt or completion of a task
    Tasks may be preempted by clock (in order to run task with higher priority)

## Slide 18: The local executive
  Buffer interface routines
    Double buffering: input buffer contains value from last iteration that will be used as input to task
    In next frame buffers are switched
  Voter routine
    Invoked by a task to get inputs for its current iteration
    Voter uses table of reconfiguration task to determine wich buffer contains copies of the output to be voted on
    If disagreement, invoke error reporter

## Slide 19: Fault detection
Each processor has its own processor/bus error table (m by n matrix) maintained by its local executive’s error handler
Entry in processor p represents the number of errors detected by processor p’s local executive that involve processor i and bus j
Suppose that processor p is reading from processor q using bus r. A matrix value change only if:
  The connection from bus r to processor q is faulty
  The connection from processor p to bus r is faulty
  Bus r is faulty
  Processor q is faulty
  Processor p is faulty
e>0 = a threshold of errors that will be tolerated for any processor/bus combination

## Slide 20: Fault detection
The connection from bus r to processor q is faulty
  Exists a bus j such that
  Exists a processor i such that
Processor p will stop using bus r to talk to processor q

## Slide 21: Fault detection
The connection from processor p to bus r is faulty
Processor p will stop using bus r and will report to the global executive that bus r is faulty
Bus r is faulty (only the global executive can distinguish this case)
Every processor will stop using bus r

## Slide 22: Fault detection
Processor q is faulty
Processor p will report to the global executive that processor q is faulty
Processor p is faulty
  Error handler cannot diagnose case 5, since the failure of the processor executing it could cause the error handler to decide that any (or none) of the other four cases hold
Global executive decides

## Slide 23: The simulator
SIFT system coded in Pascal
Avionics computer not available
Executive is being debugged on an available general purpose computer (DEC PDP-10)
A simulator has been constructed
The simulator uses five asynchronous processes, each running a SIFT executive and a «toy» set of application tasks.
Faults are injected, either at the processor or the bus levels, and a visual display of the system’s behavior is provided

## Slide 24: future works
Proof of correctness
  Operating system model
  Program model
Real testing
  When avionics computer will be available

## Slide 25: conclusions
SIFT is an attempt to use modern methods of computer design and verification to achieve fault-tolerant behavior for real-time, critical control systems.
Using standard, mass produced components helps to attain high reliability
Replication of standard components to detect and analyze errors and to dynamically reconfigure the system bypassing faulty units
Pecial hardware is needed only to isolate the units from one another
Using software to achieve fault-tolerance, SIFT allows considerable flexibility
This design has been oriented toward the needs of commercial air transports but the basic architectural approach has a wide applicability to critical real-time systems.